Design of Twiss Parameter Storage in Puffin
Jonathan Smith
24.06.2016

---
The particles live on multiple nodes so…
Slices may need particles on multiple ranks unless we require that the number of slices is an integer multiple of the number of ranks (ugly).
Probably want a single rank to write all the data, or alternatively have ranks take responsibility for slices where (say) the cell index of the start particle is controlled on that node.
Simplest implementation, is that all ranks sum
A) all slices, for
B) all phase space coordinates, all squares of all phase space coordinates, and all products of phase space coordinates.
We should calcalule ‘scaled’ emittance as a raw parameter. x,y (in universal scale – ie x,y x=x_si/sqrt(lclg)

---
Pros and cons of either storage technique
All arrays on all ranks is wasteful, but ultimately we are talking about a few tens of double precision integers only.
All arrays on all ranks is simpler to implement – all particles on that processor can be binned.
All arrays on all ranks is probably more robust – less chance to do the wrong thing in passing data over ranks
All data on all ranks simplifies the reduction onto node 0, and will allow for straight forward writing there.
Having different slices on different ranks is more complicated, so we will not do it this way.

---
File I/O:
We don’t want open file handles on crash, so each time we write the new data, we want to read the existing array… OR
We read never read back in what is already in the file, we only write out what is in memory. This could be problematic for restart, but certainly will save on IO. We just overwrite the file each time… OR
We only ever write the slice quantities right at the end. If a restart, then the user doesn’t get them.
(2.) Seems to be a decent compromise, but perhaps we should ultimately make all available with a flag to switch between. Priority is to have one of these available, so (2) is a good option. We won’t worry about restarts for now. Slice quantities should probably be read back in for restart if this is the approach to take. (1) is probably what the user expects us to do, but is probably quite inefficient.